|  | ......................... Pc. .............................. € .............................. € GEZE F 1200+ System Drive system for inward opening turn-and-tilt / bottom-hung windows for daily ventilation and exhaust. Drive system consisting of a drive unit, the F 1200+ and the F 1200 turn-and-tilt hardware. Automated tilted position to opening width of 180 mm without chain and manual opening in turning position. In disconnected mode, mechanical emergency locking and unlocking is possible. Drive with integrated operating element and handle function for motorisation of the associated hardware. The number of horizontal/vertical central locking systems depends on the closing force of the leaf. Application Leaf dimensions: ........ mm width (min. 750 mm – max. 2400 mm) ........ mm height (with vertical operation by F 1200+ min.980 mm – max. 3500 mm) (with horizontal operation by F 1200+ 750 mm – max. 3500 mm) Opening width with tilt opening: 180 mm Leaf weight: max. 200 kg (corresponding application diagram can be found in the installation drawing |
| --- | --- |
|  | ......................... Pc. .............................. € .............................. € GEZE F 1200 turn-and-tilt hardware Turn-and-tilt hardware Cranked turn-and-tilt hardware for convenient and simple operation of large and heavy aluminium windows. The hardware consists of a surface-mounted hinge side and a concealed central locking mechanism. Hardware properties Usable in aluminium profile systems Schüco, Hueck, Wicona with the following hardware chamber dimensions: Leaf groove: 21 mm Frame groove: 14 mm Groove depth push rod: 6.5 mm Rebate space: 16 mm Hardware design Colour hinge side: ( ) EV1 / ( ) according to RAL Type of installation / installation position: ( ) DIN R / ( ) DIN L |
|  | ......................... Pc. .............................. € .............................. € GEZE F 1200+ drive Ventilation drive for automation of inward opening turn-and-tilt and bottom-hung windows. Usable only with F 1200 hardware Functions: Electrical locking and unlocking of the hardware in real time with manual turn function plus motorised tilt ventilation for the ventilation mode of tilt and turn and bottom-hung windows with variable adjustment. The high quality aluminium drive unit serves as an ergonomic handle element with manual operation in the turning position. Use of the turning position can either be completely deactivated, or enabled for authorised persons only. Automatic mode enables extremely quiet-running operation. Operating unit with capacitive control keys with LED backlight enables intuitive operation with recommended actions and so prevents misuse by the user. An LED status display shows the opening indication, the operating mode as well as warnings in the event of misuse. Precise control of the operating field by means of proximity sensor to identify when the user is approaching or moving away, and brightness sensor to adjust the ambient brightness. In disconnected mode, the drive can be moved by means of mechanical emergency unlocking. Application Designed for the GEZE F 1200 tilt and turn hardware for leaf heights up to 3.5 m with a maximum leaf weight of up to 200 k (note special groove geometry and application diagrams for the hardware). Opening width with tilt opening: 180 mm Activation Manual operation via integrated operating field on the drive and integration in the building automation in conjunction with GEZE IQ box KNX possible. Installation The drive unit can be installed both vertically and horizontally. A cable transition from the frame to the leaf can be designed as divisible line transition. Pinch protection Up to protection class 3 according to the Machinery Directive EC/42/2006 without additional sensors thanks to reduced closing speed. In conjunction with GEZE IQ box Safety and suitable sensors, protection up to class 4 is possible (according to safety analysis). Technical data Supply voltage: 24 V DC / ± 10 % Current consumption: max. 2.5 A Duty rating: ED 30 % Power consumption: 60 W Ambient temperature: -5 °C to +70 °C Unlocking time: < 4 s Sound pressure level: < 38 dbA (automatic mode) Speed (tilt) automatic operation 11 mm/s on main closing edge Speed (tilt) manual up to 32 mm/s on main closing edge Housing IP rating: IP 40 Housing: aluminium Dimensions: 506 x 53 x 45 mm (W x H x D) Installation position: ( ) vertical / ( ) horizontal Surface: anodised EV1 Colour: ( ) EV1 / ( ) according to RAL.......... Side cap: ( ) RAL 7012 / ( ) according to RAL.......... Version Type of installation / installation position: ( ) DIN R / ( ) DIN L Turn function: ( ) enabled ( ) mechanical turn block (key) ( ) software-controlled turn block |
|  | ......................... Pc. .............................. € .............................. € Cable transition Concealed cable transition in the rebate space for power supply of the window drives. Cable transition with detachable connection. Application To provide power supply to drives that are mounted on the window leaf Leaf and frame installation Version ( ) Cable transition 4 m / 6 m ( ) Cable transition 2 m / 3 m |
|  | ......................... Pc. .............................. € .............................. € Power supply – NT 6.25 A – 24 V HS power supply Power supply for top hat rail mounting and to supply 24 V drives and control units. Technical data Output voltage: 24 V DC Operating voltage: 230 V +/- 10% Output current: max. 6.25 A IP rating: IP20 Version Top hat rail housing: grey Size W x H x D [mm]: 72 x 95 x 66.5 Material: plastic |
|  | ......................... Pc. .............................. € .............................. € Surface-mounted housing Housing for surface-mounted installation of top hat rail components such as power supplies or control units. With integrated 35 mm top hat rail for devices with a max. of 7 division units (18 mm). Technical data IP rating: IP 40 Cable routing surface-mounted or flush-mounted Version Size W x H x D [mm]: approx. 193 x 130 x 82 Colour: white Suitable for cascading Material: plastic |
|  | ......................... Pc. .............................. € .............................. € Delivery and installation Delivery, installation and commissioning by plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection book. |