|  | ......................... pcs. .............................. € .............................. € GEZE Slimline fanlight opener OL 90 N Activation with hand lever For daily aeration and ventilation with vertically installed rectangular windows with bottom-hung or top-hung casements, outward opening. Installation can be carried out from the front, without visible attachment screws. Casement is fitted with safety catch and locking device in the scissors. Casement closing pressure must be adjusted at the casement bracket. For window cleaning, the scissors can be disengaged quickly by pressing the release catch. Clearance-free activation via a hand lever with spring hinge reverser. Rod must be covered using an aluminium profile. Technical data: Opening width: 170mm Clear overall width: ........ mm (min. 370 mm) ( ) without locking mechanism ( ) Soffit depth 0 - 30mm ( ) Soffit depth 31 - 60mm Leaf width: ........ mm ( ) 1 scissors for casement widths from 400 - 1200 mm1) ( ) 2 scissors for casement widths from 1201 - 2400 mm1) ( ) 3 scissors for casement widths from 2401 - 3600 mm1) 1) Maximum panel weight 30kg Maximum casement weight 80kg ( ) with locking mechanism (only with soffit depth: 31mm – 60mm) Leaf width: ........ mm ( ) 1 locking mechanism, 1 scissors for casement widths from 600 – 1000 mm1) ( ) 2 locking mechanisms 1 scissors for casement widths from 1001 - 1200 mm1) ( ) 2 locking mechanisms 2 scissors for casement widths from 1201 - 1500 mm1) ( ) 3 locking mechanisms 2 scissors for casement widths from 1501 - 2400 mm1) 1) Maximum panel weight 30kg Maximum casement weight 80kg Colour: ( ) silver-coloured, EV1 ( ) white 9016 ( ) RAL ........ |
| --- | --- |